## Slide 1: Delhi E-Micromobility Planner
Methodology, data and contribution
NETWORK PLANNING PROGRAMME · NCT DELHI
Research question: How should a shared e-micromobility provider in Delhi locate hubs, battery-swap stations and riding corridors to capture the most safe, practical short-trip demand, when 96.5% of high-demand neighbourhoods have no shared e-bike service, 66% have no safety facility and 69% carry above-median traffic stress?
Notes: The whole method answers one optimisation question. The three percentages come from the grid data and define the adoption gap.

## Slide 2: Data: an analysis grid and the road network
Analysis grid
grid CSV (corrected UMVI) + sri.gpkg
2,227 hexagons, 0.66 km² each
About 120 indicators per cell
Demand, access, safety, comfort, land use, OMAS, Yulu, socio-economic
Road network
sup.gpkg · OpenStreetMap
149,135 ways, 8 road classes
23,269 km, 9.0% rated high-stress
Every distance and route uses it
PREPARATION
Join grid to geometry · percentile-rank inputs to 0–1 · split ways at shared OSM vertices · keep the largest connected network (99.6 %) · merge and simplify to 246,003 junctions and 345,601 segments · snap each cell centre to the road (median 61 m)
2,227
grid cells
19.8 M
residents
23,269 km
of road
246,003
junctions
Notes: Both datasets are in UTM 43N. 124 cells lie more than 500 m from any road and cannot be served.

## Slide 3: Methodology: nine steps in four stages
Diagnose
1
Frame the problem
Demand quintiles vs supply, safety, stress
2
Prepare data
Join, derive, rank, build road graph
Score & screen
3
Sub-indices
D, A, F, stress, G, E, battery B
4
Screen sites
Built-up, roads, water, slope → 1,563 eligible
Optimise
5
Site hubs
MCLP, 1.5 km road coverage, HiGHS
6
Swap stations
Capacitated p-median, ≤4 km, ≤400/day
7
Corridors
Calm least-cost paths between hubs
Operate
8
Fleet & battery
Trips → bikes, swaps, kWh, van loops
9
Stress-test
4 weightings → robust hubs
Suitability S = 0.35D + 0.25A + 0.25F + 0.10G + 0.05E E-bike route cost length × (1 + 1.5·high-stress) × class factor
Notes: D demand, A accessibility, F feasibility and safety, G unserved market, E equity. Class factors: trunk 1.8, primary 1.4, secondary 1.15, tertiary 1.05, service 1.1, others 1.0.

## Slide 4: Optimisation models and results
Hub siting (MCLP)
max Σ wᵢyᵢ s.t. yᵢ ≤ Σⱼ∈Nᵢ xⱼ, Σxⱼ = p
Nᵢ = cells within 1.5 km by road. p = 148 at the knee of the coverage curve; exact 77.5% vs greedy 75.6%
Swap stations (p-median)
min Σ swapsₕ × road distanceₕₛ
One station per hub, ≤ 4 km, ≤ 400 swaps/day → 25 stations, mean 2.52 km
Corridors & van loops
Dijkstra on calm cost; NN + 2-opt tours
762 km of corridor, 5.9% high-stress; 430 van-km/day
148
hubs
68.4%
residents served
51,893
trips/day
4,281
swaps/day
142/148
robust hubs
Notes: Trip potential is a planning estimate: population × 1.3 trips × 45 % short trips × 0.5 % adoption, scaled by demand. Robust hubs keep a hub within 1.5 km by road under all four weightings.

## Slide 5: Platform: planner and user tools on one model
Route designer: calm route vs shortest route on the OSM network
Planner
Suitable locations · road network & routes · battery & stations · roll-out & KPIs; live re-optimisation
User
Journey planner (walk–ride–walk, time, distance, fare) and nearest facilities by road
Build
Python (GeoPandas, SciPy, PuLP + HiGHS) offline; browser runs Dijkstra/A* on a 3.3 MB compressed road graph
Notes: Pages: Home, About, Facilities (Planner with four sub-pages, User). One self-contained page; no server needed.

## Slide 6: Contribution
Quantified adoption gap
Turns the grid into one evidence-backed research question: supply, safety and stress mismatched with demand
Road-network coverage
Hub service zones, station distances and van loops measured on 23,269 km of real roads, not straight lines
Battery logistics in the siting
Swap stations, charging load and battery pool planned together with the hubs
Stress-aware routing
Calm corridors keep 94% of riding on low-stress roads for +6% distance, and rank protected-lane priorities
Robust, transparent plan
Exact optimisation plus scenario testing: 142 of 148 hubs hold under every weighting
One tool, two audiences
Planners site and size the network; riders get route, time, fare and nearest facilities from the same model
Limits: trip potential is estimated, roads are routed both ways, POIs are per cell and fares are illustrative.
Notes: Next steps: calibrate demand with operator trip logs, add one-way rules and point POIs, and pilot the robust hubs.